## Slide 1: Power Containers: An OS Facility for Fine-Grained Power and Energy Management on Multicore Servers
Kai Shen, Arrvindh Shriraman, Sandhya Dwarkadas,
Xiao Zhang, and Zhuan Chen
University of Rochester
Shriraman is now at Simon Fraser University; Zhang is now at Google.

## Slide 2: Problem Overview and Motivation
Power/energy are important for data centers and servers
Dynamic power consumption on modern hardware
  Power proportionality: 5% idle power on Intel SandyBridge
  Workload dependency: 3:2 power ratio on same machine
A server runs many requests from users; needs per-request power accounting and control
  Request is basic unit of user-initiated work
    Carbon footprint of a web search?
    Power viruses in cloud
  Request is basic unit of load distribution

## Slide 3: Power Containers on Multicore Servers
Challenges:
  Concurrent, fine-grained request activities over multiple stages
  Complex multicore power sharing; insufficient direct measurement
Approach: event-based power modeling + request tracking
Contribution on power modeling:
  Attribute multicore shared power
  Use coarse-grain measurement to enhance power model online
Contribution on request tracking:
  Online OS request tracking/control; transparent to applications

## Slide 4: Multicore Power Attribution to Concurrent Tasks
Bellosa’s event-based power model
  Assumes direct, linear relationship between one’s power and physical activities (instructions, cache references, bus activities, …)
On a multicore, maintenance of shared resources consumes certain power when at least one core is active
  Attribution of such shared power is not affected by one’s own physical activities, but rather depends on the level of multicore sharing
  Our approach: evenly attribute to concurrently running requests
  Implemented efficiently by local estimation of multicore sharing level (to avoid expensive global coordination and cross-core interrupts)

## Slide 5: Measurement-Assisted Online Model Correction
Event-based power model is questioned on today’s system
  [McCulough et al. 2011] showed poor results
  We find large model errors due to different characteristics between production and calibration workloads (worse for unusual workloads)
Our approach
  Coarse-grain power measurement can help re-calibrate power model
  Measurement has delays, needs alignment with modeled power

## Slide 6: Request Power Accounting
Request context tracking in a multi-stage server
  Past techniques are not in-band [Magpie/X-Ray], or at app/library level [Google Dapper]
Our approach
  [X-Trace] net flow tracking
  Track request propagation events (sockets, forks, sync, …) at the OS
  Attribute and control power at proper request context

## Slide 7: Online Overhead
Overhead depends on frequency of periodic activities; low overhead (<1%) for sufficiently frequent activities
Periodic maintenance of an active power container
  Reading hardware counters, power modeling, updating request stats  2948 cycles, 1656 instructions, 16 floating point ops, 3 LLC refs  1µsec, 10 µJs
Measurement-assisted online model recalibration
  Computation of least-square linear regression (16µsecs for ~30 samples)

## Slide 8: Request Power/Energy Accounting Results
Distribution of average request power
Distribution of request energy usage

## Slide 9: Validation of Request Power Accounting
Challenge of validation:
  Hard to know the ground truth – no way to directly measure request power or energy use on a multicore server
Validation approach #1:
  Aggregate accounted request energy over a time duration to estimate total system energy usage; then match with measurement
  No more than 9% error across six workloads on three machines
Validation approach #2:
  Use accounted request energy to estimate system energy usage at hypothetical workload conditions (different mixes/rates of requests)
  No more than 11% error for workloads with stable-behavior requests

## Slide 10: Per-Request Power Control
Cap max power use of a server machine
  Set equal per-request power budget for fairness
  Power containers track request power usage, throttle high-power requests using core duty-cycle modulation
A case study of Google App Engine with power viruses
  Power containers: 33% slowdown for power viruses; 2% slowdown for normal requests
  Alternatively slow down all requests indiscriminately (13%) to lower the max power

## Slide 11: Heterogeneity-Aware Request Distribution
Different workloads/requests exhibit different levels of machine preferences in energy efficiency
  Energy usage on Intel SandyBridge over energy usage on Woodcrest
Power containers can capture fine-grained request energy profiles and distribute load in a server cluster for high efficiency
  Case study shows 25% energy saving compared to alternatives

## Slide 12: Conclusions
High-level messages:
  Fine-grained power accounting and control are important for multicore server efficiency and dependability
    Increasingly so on more power-proportional hardware and dynamic-behavior, user-controlled workloads (web 2.0, cloud computing, …)
  Possible to support these at the OS (low overhead on today’s processor hardware, requiring no application assistance)
Contributions:
  Enhanced modeling to account for multicore shared power
  Use online measurement to mitigate power model inaccuracy
  OS-level online request power tracking and control
  Utility in power virus control and adaptive request distribution